## Slide 1
KAT Aluminium Doors and Windows
Windows
Sliding Doors
Bifolding Doors
Entrance Doors
Art Deco Doors and Windows
Skip To:

## Slide 2
Aluminium Casement Windows

## Slide 3
Features
72mm frame depth
Slim sight lines brick to glass – 88mm
Exclusive Hi-Reflex spacer bar thermal break technology
Maximum sizes:
  Top hung 1600mm x 1750mm
  Side hung 845mm x 1600mm
Window U-Value 1.4 with centre pane of 1.2
Externally beaded – square bead
Aluminium Casement Windows

## Slide 4
Options
Shaped fixed frames
Windows can be side hung, top hung or fixed
Corner posts and bay solutions
28mm and 36mm Chamfered bead
32mm Square bead
Windows can be internally beaded
Aluminium Casement Windows

## Slide 5
Colours
Anthracite Grey in a luxurious Textura
finish from stock
A wide range of RAL colours in Textura, Matt
or Gloss finish are available
Aluminium Casement Windows

## Slide 6
Hardware
Push button locking handles available in:
Black
White
Gold
Satin Chrome
Polished Chrome
Aluminium Casement Windows

## Slide 7
Section through drawings
Aluminium Casement Windows

## Slide 8
Aluminium Tilt Turn Windows

## Slide 9
Features
72mm deep frame front to back
79mm Slim sight lines brick to glass across
frame and sash
Square bead – externally glazed
Maximum sash 1600mm x 2100mm
Full window U-Value 1.4 with centre pane of 1.2
Aluminium Tilt Turn Windows

## Slide 10
Options
Can meet PAS 24
Fixed post and variable bay solutions
Aluminium Tilt Turn Windows

## Slide 11
Colours
Anthracite Grey in a luxurious Textura
finish from stock
A wide range of RAL colours in a Textura, Matt
or Gloss finish are available
Aluminium Tilt Turn Windows

## Slide 12
Hardware
Inox Silver
White
Aluminium Tilt Turn Windows

## Slide 13
Section through drawings
Aluminium Tilt Turn Windows

## Slide 14
Aluminium Inline Sliding Doors
AA4110

## Slide 15
Features
Sash widths up to 1.5m wide and 2.2m high
5 point enhanced security lock
Adjustable tandem rollers to ensure sashes run smoothly
Stainless steel wheels and tracks
87mm meeting style
28mm, 32mm or 36mm glazing
Aluminium Inline Sliding Doors

## Slide 16
Hardware
Luxury cranked 400mm bar handle
internally and externally
Lever latch and escutcheon internally and externally
Optional:
1000mm bar handle to replace 400mm
Finger pull externally with 400mm or 1000mm
handles internally
No lever latch or escutcheon externally
Aluminium Inline Sliding Doors

## Slide 17
Colours
Anthracite Grey in a luxurious Textura
finish from stock
A wide range of RAL colours and finishes
are available
Aluminium Inline Sliding Doors

## Slide 18
Section through drawings
Aluminium Inline Sliding Doors

## Slide 19
Features
Twin track
  Frame depth 113mm
  196mm Cill
  2, 3 or 4 pane options
Triple track
  Frame depth 175mm
  249mm Cill
  3 or 6 pane options
Optional - Flush Floor Receptor
Aluminium Inline Sliding Doors

## Slide 20
Aluminium Lift and Slide Doors
AA4110

## Slide 21
Door sashes span up to 3m wide and up to 2.6m high (subject to max sash weight 300kgs)
Stainless steel wheels and tracks
107mm meeting style
28mm, 32mm* or 36mm glazing
Cills and frame depth are the same for Inline
and Lift & Slide
*32mm triple glazing available if overall glass dimension is less than 2.4m²
Aluminium Lift and Slide Doors

## Slide 22
Hardware
250mm brushed steel Lift & Slide handle to inside
Stainless steel track
Max sash weight 200kgs
Optional
Brushed steel Lift & Slide handle to outside
Finger pull to outside
Aluminium Lift and Slide Doors

## Slide 23
Colour Options
Anthracite Grey in a Textura finish from stock
Wide range of RAL colours and finishes available
Aluminium Lift and Slide Doors

## Slide 24
Opening Configurations
Aluminium Lift and Slide Doors

## Slide 25
U Values
Aluminium Lift and Slide Doors

## Slide 26
Features
Twin track
  Frame depth 113mm
  196mm Cill
  2, 3 or 4 pane options
Triple track
  Frame depth 175mm
  249mm Cill
  3 or 6 pane options
Optional – Flush Floor Receptor
Aluminium Lift and Slide Doors

## Slide 27
Aluminium Super-Size Sliding Doors
AA3572

## Slide 28
Aluminium Super-Size Sliding Doors
Features
Door sashes up to 3m x 3m
Contemporary square bead
U Value 1.3 W/m2K with 28mm double glazing
100mm meeting style
Multi-point locking
42mm Standard fully weathered threshold

## Slide 29
Aluminium Super-Size Sliding Doors
Colours
Anthracite Grey in a luxurious
Textura finish from stock
A wide range of RAL colours and
finishes are available

## Slide 30
Aluminium Super-Size Sliding Doors
Dimensions
Twin Track
  164mm frame depth
  190mm Stub Cill / 250mm Cill
Triple Track
  256mm frame depth
  250mm Stub Cill / 290mm Cill

## Slide 31
Aluminium Super-Size Sliding Doors
Opening configurations
Twin Track, 2 or 3 panes
Triple Track 3 panes

## Slide 32
Aluminium Super-Size Sliding Doors
Hardware
Handle is rotated 180° to open the doors
Brushed Stainless Lift & Slide handle
internally and externally as standard
Optional
Lift & Slide handle internally only
Finger pull externally to replace Lift &
Slide handle

## Slide 33
Aluminium Slim Sliding Doors
Visoglide plus

## Slide 34
Aluminium Slim Sliding Doors
Features
Slim 35mm sightlines
Available as Inline Slider or Lift & Slide
U Values from 1.6 W/m2k
28mm glazing as standard with square bead
2, 3 or 4 sash options

## Slide 35
Aluminium Slim Sliding Doors
Colours and Hardware
Wide range of RAL colours and finishes
Off-set ‘D’ handle in Black, White or Silver
as standard.
Handles can be colour-matched to the
door profile if requested.

## Slide 36
Aluminium Slim Sliding Doors
Section through drawings

## Slide 37
Aluminium Slim Sliding Doors
Dimensions of Inline Sliding Doors Max sash height: 2500mm Providing sashes are within max sash weight of 200kgs, there is no maximum width. Lock will have two locking points where sash is below 1400mm. For PAS24:2012 the minimum height is 1885mm. | Dimensions of Lift & Slide Doors Max sash width: 3294mm Min sash height: 1718mm Max sash height: 2500mm Max sash weight: 300kgs

## Slide 38
Aluminium Bifold Doors

## Slide 39
Features
From 1 to 7 panels in various configurations
Inward or outward opening
Standard fully weathered threshold 45mm
  Low threshold option 24mm
3 star diamond security rated cylinder with Kitemark
PAS24:2016 enhanced security available
28mm Square glazing bead as standard
Sits on 104mm, 159mm and 199mm cills
Aluminium Bifold Doors

## Slide 40
Colour Options
Anthracite Grey in a luxurious Textura finish from stock
Wide range of RAL colours and finishes are available
Aluminium Bifold Doors

## Slide 41
Hardware
Master handles with design exclusive to KAT. Available in White, Grey, Black, Chrome, Gold and Brushed Steel, with a 10 year guarantee.
Locking intermediate lever handle available in White, Black, Chrome and Brushed Steel finish.
A Black ‘D’ handle
is also fitted to all Bifold Doors.
Aluminium Bifold Doors

## Slide 42
Configuration Options
On styles marked with an #, there is no traffic door and doors can only be opened from inside the property.
Aluminium Bifold Doors

## Slide 43
 | Maximum | Minimum
Height | 2900mm depends on width | 1800mm
Overall width | 840mm | 1400mm based on 2 panels
Panel width | 1200mm | 700mm
Weight per panel | 120 Kgs | 
Size limits
Max Sash Width 1200mm
Aluminium Bifold Doors

## Slide 44
Sightline
Glass to glass sightline is 145mm
Aluminium Bifold Doors

## Slide 45
Part L1B/L2B | OPEN IN OR OPEN OUT FSD |  |  |  |  | 
 | Panel Variant |  |  |  |  | 
Glass U Value (W/m²K) | 2 Panel | 3 Panel | 4 Panel | 5 Panel | 6 Panel | 
1.2 | 1.54 | 1.52 | 1.51 | 1.50 | 1.50 | 
1.1 | 1.47 | 1.44 | 1.44 | 1.43 | 1.43 | 
1.0 | 1.40 | 1.37 | 1.36 | 1.35 | 1.35 | 
0.9 | 1.32 | 1.29 | 1.29 | 1.28 | 1.28 | Door U Value
0.8 | 1.25 | 1.22 | 1.21 | 1.20 | 1.20 | 
0.7 | 1.18 | 1.15 | 1.14 | 1.13 | 1.12 | 
0.5 | 1.03 | 1.0 | 0.99 | 0.98 | 0.97 | 
U Values
Aluminium Bifold Doors

## Slide 46
Aluminium French Doors
.

## Slide 47
Features
Standard fully weathered threshold*
Frame depth 72mm front to back
3 hook multi-point lock
Square 28mm glazing bead as standard
3 star cylinder with Kitemark
Sits on 104mm, 159mm and 199mm cills*
* product in development currently
Aluminium French Doors
.

## Slide 48
Optional
32mm & 44mm square bead options
24mm Low threshold option is fully weathered
PAS24:2016 enhanced security
Aluminium French Doors
.

## Slide 49
Hardware
Lever handles fitted to Master and Slave door with design exclusive to KAT. *
Available in White, Grey, Black, Chrome, Gold and Brushed Steel, with a 10 year guarantee.
Aluminium French Doors

## Slide 50
Colour Options
Anthracite Grey in a luxurious Textura finish from stock
Wide range of RAL colours and finishes are available
Aluminium French Doors

## Slide 51
Belvedere Entrance Doors

## Slide 52
Designs available
5 contemporary designs in Anthracite Grey Matt -from stock
Belvedere Entrance Doors

## Slide 53
Hardware
1000mm Cranked bar handle in Brushed Steel finish to inside and outside
Thumbturn to inside
Belvedere Entrance Doors

## Slide 54
Features
72mm door frame depth
5 point locking hook lock
3 star cylinder with Kitemark
Severe weather tested 45mm threshold
Double glazed units with satin obscured glass
Belvedere Entrance Doors

## Slide 55
Dimensions
Max outerframe size 986mm wide by 2,184mm high with standard threshold
1,054mm wide x 2,218mm high with 34mm add-on option
Side lights and top lights available
Belvedere Entrance Doors

## Slide 56
Art Deco Doors

## Slide 57
Features
59mm slim frame
Available as single doors or double doors
47mm frame depth front to back
U-Value of 1.5 with a double glazed unit
Weather test results:
  Air 600pa Water 600pa Wind 2400pa
Art Deco Doors

## Slide 58
Hardware
Handles are available in a wide range of colours and finishes, including:
  Anodised shades of gold, bronze, silver, grey and black or textured anthracite grey.
Art Deco Doors

## Slide 59
Security
On double doors, one pair of handles is fitted to the master door sash, with a face mounted shoot bolt to secure the slave door.
Multi-point locking
3 Star security cylinder
Art Deco Doors

## Slide 60
Threshold and Cills
33mm Standard fully weathered threshold
Cills available in 85mm, 135mm, 150mm, 190mm, 225mm or 300mm
Art Deco Doors

## Slide 61
Art Deco Windows

## Slide 62
Features
Slim 59mm sightline
U-Value down to W/m2K 1.5 with double glazed unit
47mm slim frame depth
Art Deco Windows

## Slide 63
Hardware
A full suite of handle options is available to match KAT’s Art Deco doors, with Victorian and Art Deco styles including:
  ‘Monkey Tail’ or ‘Bulb End’
Handles available in any RAL colour, or anodised:
  gold, bronze, silver, grey and black.
Art Deco Windows

## Slide 64
Options
PAS 24 Security
Windows can be side hung, top hung, fixed
or tilt and turn
Arched head and circular shaped windows available
Can be internally beaded if preferred
Art Deco Windows

## Slide 65
KAT Aluminium Doors and Windows
Windows
Sliding Doors
Bifolding Doors
Entrance Doors
Art Deco Doors and Windows
Skip To: